| Title | Construct and maintain a basic residential fence and gate as a BCATS project |
| --- | --- |
| Level | 2 | Credits | 7 |

| Purpose | This unit standard has been designed to be achieved in a building, construction and allied trades skills (BCATS) programme. People credited with this unit standard are able to: calculate quantities and prepare an order for materials; construct and perform routine maintenance on a basic residential timber fence; construct and install a basic timber residential gate; and complete work operations. |
| --- | --- |

| Classification | Construction Trades > Building, Construction, and Allied Trades Skills |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

BCATS project refers to a project undertaken in a BCATS environment under general supervision, using a range of tools, equipment and materials, and involving standard processes.

BCATS environment refers to any workplace or context where work or activities related to the building, construction and allied trades sector take place, such as school workshops, training establishments, outdoor areas, and industry placement workplaces.

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following: manufacturers’ specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

Working drawings are the set of drawings associated with a construction project, and can include plans, elevations, sections, details or any other drawings that give information about the project.

Workplace practice refers to the procedures specific to a BCATS environment, which cover the standard and required practices of that environment.

2	Assessment against this unit standard may occur in any BCATS environment.

3	Evidence is required for a fence with a minimum length of 4.8 metres (three posts).

4	Legislation relevant to this unit standard includes:

Health and Safety at Work Act 2015;

Health and Safety at Work Regulations 2016.

Outcomes and performance criteria

Outcome 1

Calculate quantities and prepare an order for materials for a basic residential fence and gate.

Performance criteria

1.1	Quantities of materials are calculated from working drawings and job specifications.

1.2	An order for materials is prepared in accordance with workplace practice.

Outcome 2

Construct a basic residential timber fence.

Performance criteria

2.1	Post positions are set out, and post holes are excavated in accordance with working drawings and job specifications.

2.2	Posts and rails are set up and fixed in accordance with working drawings and job specifications.

2.3	Cladding is fixed and the fence is finished in accordance with working drawings and job specifications.

Range	one of – timber palings, sheet metal.

Outcome 3

Construct and install a basic timber gate in a residential fence.

Performance criteria

3.1	Gateway is measured and gate constructed in accordance with working drawings and job specifications.

3.2	Gateposts are plumbed and placing of hinges marked on gatepost and gate.

3.3	Hinges are installed on gate, and gate is installed in accordance with working drawings and job specifications.

3.4	Installed gate swings clear of the ground throughout its arc.

3.5	Latch hardware is installed and operates according to design and manufacture.

Outcome 4

Perform routine maintenance on a basic residential timber fence.

Performance criteria

4.1	Fence is checked for damage and wear.

4.2	Damaged or worn components are replaced in accordance with workplace practice.

Outcome 5

Complete work operations.

Performance criteria

5.1	All operations are safely completed in accordance with workplace practice.

5.2	Workplace, tools, plant and equipment are cleaned, and tools, plant and equipment are stored in accordance with workplace practice.

| Replacement information | This unit standard was replaced by unit standard 31860. This unit standard replaced unit standard 12934. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 27 October 2005 | 31 December 2018 |
| Review | 2 | 14 December 2007 | 31 December 2018 |
| Rollover and Revision | 3 | 20 October 2016 | 31 December 2019 |
| Review | 4 | 25 July 2019 | 31 December 2020 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.